# Surrogate CMA-ES

Algoritmus
Parameters
- how long the model should be used (let CMA-ES converge to the optimum alone...?)
- evolution control (either individual or generational) and its parameters (\gamma for individual (also affected by \beta), resp. generations = [original, model] -evaluated)
- \beta – max. fraction of normal population size (\lambda) to pre-sample (fraction of individuals to be evaluated by the original fitness before model training)
- \gamma – (\gamma \lambda) points are sampled for model evaluation
- model_options
CMA-ES parameters
x_start, \sigma_init, fitness()

Options
- CMA-ES
  - lambda
  - ..., 'surrogateoptions', surrogateOpts, ... - options for the surrogate modelling
  - fitargs – varargin parameters for the s_cmaes()
- surrogateOpts
  - evoControl – evolution control {'none' | 'individual' | 'generation'}
    if 'none' is selected, sampleFcn has to be set to the sampling function
  - sampleFcn – handle to the sampling function {@sampleCmaes | []}
  - sampleOpts
    - counteval
    - CMA-ES internal state and settings variables
  - modelType – string identifying type of model {'gp' | 'rf'}
  - modelOpts – model-dependent options for the model
  - evoControlTrainRange – how far to search for training points in the archive, the number is a multiplicator of \sigma
- surrogateOpts for Generation EC:
  - evoControlInitialGenerations – how many original-evaluated gens. at the beginning {0}
  - evoControlOrigGenerations – how many original-evaluated gens. in each EC phase {1}
  - evoControlModelGenerations – how many model-evaluated gens. in each EC phase {1}
  - evoControlValidatePoints – in how many points check the true fitness when using model in generation EC (model-evaluated generations)
- surrogateOpts for Individual EC:
  - evoControlPreSampleRatio – how many % of the points to sample and evaluate before training the model in individual-based EC
  - evoControlIndividualExtension – how much more points to sample before chosing promising points for original re-evaluation
  - evoControlBestFromExtension – how many % of points with the best model-fitness to choose from the “extended population” to become a part of the final population and to be original re-evaluated

ToDo
adaptive control of evoControlOrigGenerations : evoControlModelGenerations

Initialization
model = []

Generation loop
1. for g = 1, 2, ... // generation loop
    ...
    // this is individual control:
2. model = SpecificModel.new(model, model_options, x_mean, g)
3. n_required = model.getNTrainData	// zero is possible, old model is then taken
4. n_preSample = floor( \beta \lambda )
5. [X_train, y_train] = archive.getDataNearPoint( ...
        (n_required – n_preSample), x_mean, trainRange, \sigma, BD)
6. n_toSample = n_required – size(X_train,1)
7. if (n_toSample > n_preSample)
8. // either use an old model (see Drawing 1), or do not use model at all
9. if (n_toSample > 0)
10. [X_sampled, y_sampled] = dataSelector.sampleNewData( ...
           n_toSample, x_mean, sigma, BD)
11. X_train = [X_train; X_sampled]; y_train = [y_train; y_sampled]
12. model.train(X_train, y_train)
13. // sample extended population of sz. \lambda_surrogate = \gamma (\lambda – n_toSample)
     X_extend ~ \sigma B D N(0, 1) (\lambda_surrogate–times)
14. y_extend = model.predict(X_extend)
15. while not enough valid-fitness points evaluated do
16. [X_reeval, X_extend, y_extend] = surrogateSelector.select(X_extend, y_extend)
17. y_reeval = fitness(X_reeval)
18. X = [X_sampled; X_reeval]; y = [y_sampled; y_reeval]
19. archive.save(X, y)
     ...
     // this is generation control:
20. X ~ \sigma B D N(0, 1) (\lambda–times)
21. if (g is a original-evaluated generation)
22. y = fitness(X)
23. archive.save(X, y)
24. n_required = model.getNTrainData
25. if ( length(y) < n_required)
26. // try to get more data from previous generations
27. gens = indices of the last continuously original-evaluated generations
28. [X, y] = get data from generations(gens)
29. if (g is a model-building generation, i.e. last of the original-evaluated)
30. if (length(y) >= n_required)
31. model = SpecificModel.new(model, model_options, x_mean, g, n)
32. model.train(X, y)
33. else
34. // mark the next generation as “original-evaluated” and “model-building”
35. else // g is a model-evaluation generation
36. y = model.predict(X)

Open problems
- test whether enlarging \sigma when using surrogate model helps
- when should we stop using surrogate modelling? at specific \sigma-value? at specific generation? ...?
- try (maybe :) enlarging the training set for generation-EC model building with old data modified by affine translation to the new mean
  Drawing 1: Affine translation of the old population